## Slide 1
AI-Based Surrogate Modeling for Finite Element Analysis
Replacing Expensive FEA Simulations with Graph Neural Networks for Rapid Parametric Design Optimization
Yonatan Reinstein
1/14

## Slide 2
The Problem: FEA is a Bottleneck
▸ FEA solves PDEs on meshes to predict stress, displacement, etc.
▸ Each ANSYS simulation takes seconds to minutes per design
▸ Design optimization requires evaluating thousands of candidates
▸ Brute-force search over parametric dimensions is infeasible
▸ Goal: train a fast surrogate model that approximates FEA with orders-of-magnitude speedup
Traditional vs. Surrogate
Traditional: dims → CAD → Mesh → ANSYS → stress ~30 sec per design × 10,000 designs = ~83 hours
Surrogate: dims → Neural Network → stress ~5 ms per design × 10,000 designs = ~50 seconds
2/14

## Slide 3
System Overview: Four-Stage Pipeline
1. Data Generation
Parametric CAD → IRIT Mesh → ANSYS FEA → Graph Dataset
▶
2. Model Training
GNN / MLP Surrogate learns FEA mapping
▶
3. Optimization
Genetic Algorithm uses surrogate for fast evaluation
▶
4. Evaluation
Compare candidates Visualize results Verify with FEA
The surrogate model is trained offline on FEA data, then used online during optimization to evaluate thousands of design candidates in seconds instead of hours.
3/14

## Slide 4
Stage 1: Data Generation
▸ IRIT parametric CAD model defines geometry from dimensions (e.g., 36 parameters d1–d36 for the "arm" geometry)
▸ Random sampling of dimension values within bounds (uniform distribution, seeded for reproducibility)
▸ IRIT generates hex/tet mesh for each parameter set
▸ ANSYS MAPDL runs FEA simulation: • Material: Steel (E = 200 GPa, ν = 0.3) • BCs: anchored base + applied tip load (1 MN) • Output: von Mises stress, displacement at every node
▸ Parallel execution: 4 MAPDL instances with retry logic
▸ ~1000–3000 samples generated per geometry
Pipeline per Sample
dims = {d1: 0.41, d2: 0.73, ..., d36: 2.20} ↓ IRIT CAD model → volume = 17.87 m³ ↓ Hex mesh (10×10×20) → 2000+ nodes ↓ ANSYS MAPDL solve ↓ Per-node: [Ux, Uy, Uz, σ_vm] Global: max_stress = 7.36e7 Pa max_disp = 0.0012 m
4/14

## Slide 5
Background: Neural Networks in 60 Seconds
▸ A neural network is a parametric function f(x; θ) → y
▸ Composed of layers: each applies a linear transform followed by a non-linear activation (e.g., ReLU)
▸ Training = finding θ that minimizes a loss function L(θ) = ∑ || f(xᵢ; θ) - yᵢ ||² (mean squared error)
▸ Optimization via gradient descent: θ ← θ - α · ∇L(θ) (backpropagation computes gradients)
▸ Universal approximation: with enough parameters, can approximate any continuous function
▸ Key advantage: once trained, inference is O(ms) vs. O(seconds) for FEA
MLP: Multi-Layer Perceptron
Input (36 dims) ↓ Linear(36, 128) + ReLU Hidden (128) ↓ Linear(128, 128) + ReLU Hidden (128) ↓ Linear(128, 3) Output: [volume, stress, displacement]
The MLP takes dimension values as a flat vector and directly predicts global outputs. Simple and fast, but ignores the spatial/mesh structure.
5/14

## Slide 6
Key Insight: FEA Meshes Are Graphs
▸ A FEA mesh is naturally a graph: nodes = vertices, elements define edges
▸ Each node carries features: position (x,y,z), forces (Fx,Fy,Fz), boundary flag
▸ Each node has labels from FEA: displacement (Ux,Uy,Uz) and stress (σ_vm)
▸ This is exactly the structure Graph Neural Networks are designed to process
Graph Data Object (PyTorch Geometric)
Data( x = [N, 7] # node features [x, y, z, Fx, Fy, Fz, anchored] edge_index = [2, E] # bidirectional edges volume = scalar # graph-level label max_stress = scalar # graph-level label dims = [1, 36] # parametric dimensions )
Why Graphs Instead of Flat Vectors?
▸ Spatial locality: stress depends on neighboring nodes
▸ Variable mesh sizes: graphs handle any number of nodes
▸ Topology-aware: captures connectivity, not just coordinates
▸ Physically meaningful: mirrors how FEA itself works
6/14

## Slide 7
The GNN Surrogate Model
Architecture Overview
Node features [N, 7] ↓ Encoder MLP: 7 → 128 → 128 ↓ 6× EdgeConv layers (with residual connections) Each layer: hᵢ = hᵢ + EdgeConv(hᵢ, edges) EdgeConv aggregates neighbor info via: MLP([hᵢ || hⱼ], 128, 128), aggr = max ↓ Head MLP: 128 → 128 → 1 (per-node prediction) ↓ Global Max Pool: aggregate all nodes → 1 scalar ↓ Output: predicted max stress
Key Concepts Explained
▸ EdgeConv: for each node, concatenate its features with each neighbor's features, apply MLP, take max → learns edge-level interactions
▸ Residual connections: h = h + conv(h) → preserves information across layers → stabilizes training of deep networks
▸ Message passing: each layer lets nodes "communicate" with neighbors → after 6 layers, information has propagated 6 hops across the mesh
▸ Global max pool: reduces variable-size node predictions to a single graph-level output (analogous to taking max stress over all nodes)
7/14

## Slide 8
EdgeConv: Learning from Neighbors
EdgeConv is the core building block. Think of it as: each mesh node looks at its neighbors, computes a learned function of the pair, and aggregates the results.
Mathematical Definition
For node i with neighbors N(i): hᵢ' = MAX { MLP( [hᵢ || hⱼ] ) } j ∈ N(i) [hᵢ || hⱼ] = concatenation of features MLP = learnable non-linear function MAX = element-wise maximum over neighbors
Physical Analogy
▸ Similar to how FEA assembles element stiffness: each element contributes to its nodes' equations
▸ EdgeConv: each edge contributes a learned message to its endpoint nodes
▸ Max aggregation picks the dominant influence (like max stress being determined by the most stressed neighboring element)
▸ After 6 layers: each node's representation encodes information from a 6-hop neighborhood in the mesh
8/14

## Slide 9
Stage 2: Training the Surrogate
Training Setup
▸ Dataset: ~3000 FEA simulations stored as graphs
▸ Split: 80% training / 20% validation (random)
▸ Loss function: Mean Squared Error (MSE) L = || predicted_stress - true_stress ||²
▸ Optimizer: AdamW (lr = 0.002, weight_decay = 1e-4) → Adam with decoupled weight regularization
▸ Scheduler: StepLR (step=20, γ=0.9) → learning rate decays every 20 epochs
▸ Normalization: features & targets scaled to ~unit range (forces /1e6, stress /1e6 → work in MPa & MN)
Training Convergence
Epoch 1: train_loss = 0.980 val_loss = 0.95 Epoch 10: train_loss = 0.087 val_loss = 0.09 Epoch 25: train_loss = 0.031 val_loss = 0.03 Epoch 50: train_loss = 0.019 val_loss = 0.02 → ~98% reduction in prediction error → val ≈ train: model generalizes well (no overfitting)
What the Model Learns
▸ Mapping from mesh geometry + BCs → stress field
▸ Implicitly learns material response without PDEs
▸ Trained model runs in ~5 ms vs. ~30 s for ANSYS
9/14

## Slide 10
Two Surrogate Approaches: MLP vs. GNN
MLP (Multi-Layer Perceptron)
▸ Input: flat vector of 36 dimension values
▸ Output: [volume, stress, displacement]
▸ Architecture: 36 → 128 → 128 → 3
▸ Total parameters: ~21,000
▸ Ignores mesh structure entirely
▸ Pro: very fast, simple, no mesh needed at inference
▸ Con: cannot generalize to different topologies; treats geometry as a black box
GNN (Graph Neural Network)
▸ Input: full mesh graph (nodes + edges + features)
▸ Output: predicted max stress (scalar)
▸ Architecture: Encoder + 6×EdgeConv + Head + Pool
▸ Total parameters: ~400,000
▸ Exploits spatial structure of the mesh
▸ Pro: topology-aware, mirrors FEA structure; physically meaningful representations
▸ Con: requires mesh generation at inference; more expensive to train and evaluate
10/14

## Slide 11
Stage 3: Genetic Algorithm Optimization
Algorithm
▸ Population: 200 individuals (each = 36 dimensions)
▸ Generations: 400 evolutionary cycles
▸ Selection: tournament (k=2), top 80% survive
▸ Crossover: blend α·p1 + (1-α)·p2, α ∈ [0.3, 0.7]
▸ Mutation: Gaussian noise, σ = 5% of range per-gene probability = 16% rate adapts upward after gen 100
▸ Elitism: top 4 individuals preserved unmutated
▸ Checkpointing: population saved every generation
Multi-Objective Fitness
Fitness = 0.49 · V_norm (minimize volume) + 0.49 · S_norm (minimize stress) + 0.02 · (1 - D_norm) (maintain diversity) Stress constraint (soft penalty): penalty = max(σ - σ_yield, 0) · weight added to volume score All objectives normalized to [0, 1]
The GA uses the surrogate for evaluation: each generation evaluates 200 designs in milliseconds. Without the surrogate, this would require 200 ANSYS simulations per generation × 400 generations = 80,000 simulations.
11/14

## Slide 12
The Synergy: Surrogate + Evolutionary Search
▸ The GA does not need gradients of the objective → works even though mesh generation is non-differentiable
▸ The surrogate replaces the expensive inner loop (FEA evaluation) with a fast forward pass
▸ Cost comparison: 200 pop × 400 gen = 80,000 evaluations
┌───────────────────────┬────────────────────┬────────────────────┐ │ │ ANSYS FEA │ GNN Surrogate │ ├───────────────────────┼────────────────────┼────────────────────┤ │ Time per evaluation │ ~30 seconds │ ~5 milliseconds │ │ 80,000 evaluations │ ~28 days │ ~7 minutes │ │ Requires ANSYS license │ Yes │ No │ │ Accuracy │ Ground truth │ Approximation │ │ Mesh-aware │ Yes │ Yes (GNN) / No (MLP) │ └───────────────────────┴────────────────────┴────────────────────┘
12/14

## Slide 13
Technical Stack & Project Structure
Technologies
▸ Deep Learning: PyTorch + PyTorch Geometric
▸ FEA Solver: ANSYS MAPDL 25.1 (parallel pool)
▸ CAD Engine: IRIT Geometric Modeler
▸ Optimization: Custom GA (NumPy)
▸ Visualization: PyVista
▸ Compute: HPC cluster (PBS job scripts)
Project Layout
ai_fea_surrogate/ ├── core/ # Mesh, Component, IRIT │ ├── component.py # Geometry → Graph conversion │ ├── mesh.py # MAPDL interface, mesh ops │ └── IritModel.py # Parametric CAD wrapper ├── utils/ # Model definitions │ ├── gnn_surrogate.py # GNN architecture │ └── mlp_surrogate.py # MLP architecture ├── training/ # Data gen & training ├── evaluators/ # Inference wrappers ├── optimization/ # GA + fitness └── data/{geometry}/ # Per-geometry configs ├── CAD_model/ # dims.json, material ├── dataset/ # Generated .pt files └── checkpoints/ # Trained models
13/14

## Slide 14
Summary & Future Directions
What We Built
▸ End-to-end pipeline: parametric CAD → FEA data → surrogate training → design optimization
▸ GNN surrogate that respects mesh topology
▸ ~6000× speedup over direct FEA evaluation
▸ Multi-objective GA finds low-volume, low-stress designs
▸ Modular: supports multiple geometries & evaluators
Possible Future Directions
▸ Predict full stress fields (per-node), not just max
▸ Active learning: let the GA request new FEA data in regions of high uncertainty
▸ Transfer learning across geometries
▸ Mesh-free approaches (e.g., neural operators)
▸ Uncertainty quantification for surrogate predictions
Core idea: leverage the structural similarity between FEA meshes and graph neural networks to build a fast, topology-aware surrogate that enables efficient design space exploration.
14/14